## Slide 1: Re-Inventing Your Convenience Site Program
Friday, August 27, 2021 8:00 – 8:30 am
Jeffrey Murray | PE, BCEE, HDR Landfill Practice Lead
Joseph Fitzpatrick | Wake County Recycling and Compliance Coordinator
Chrissie Koroivui | Durham County Solid Waste Program Manager
Panel Discussion
Notes: Ask questions via Chat and we can answer them at the end

## Slide 2
Wake County Program
02
Durham County Program
04
Challenges
05
Lessons Learned
AGENDA
01
03
Improvements
06
Questions

## Slide 3: Wake County, North Carolina Facilities
The Solid Waste Management Division manages 19 facilities serving over 1.1 million people:
  11 Convenience Centers
  3 Household Hazardous Waste Facilities (HHW)
  3 Multi-Material Recycling Facilities (MMRF)
  1 Active (MSW) Landfill and 1 Transfer Station
  Monitors and Maintains 4 Closed Landfill Facilities
Notes: Enterprise funded
Operations outsourced

## Slide 4: Convenience Centers
11 Convenience Centers
Sites were located, designed and constructed in the early to mid 1980’s
  Minimize illegal dumping
  Encourage recycling
  Open to County & Municipal residents
  Six sites accept segregated C&D waste
  Two sites accept electronics(weekend)
  One site accepts white goods
  Funded by residents ONLY ($20/year household fee), so no commercial use allowed

## Slide 5: Convenience Centers
Since opening, the County’s population has tripled, and municipal limits have expanded.
In 2005, County began investigating waste disposal demands and functionalities of the sites
Completed 2020 Comprehensive Solid Waste Management Plan
2017 and 2020 user studies conducted

## Slide 6
Multi-Material Recycling Facilities
Three sites accepting items banned from landfill (electronics, tires & appliances)
Also takes cardboard, engine oil, rigid plastics, etc…
Open to all Wake County residents and businesses
Household Hazardous Waste Facilities
Three sites built to provide safe disposal of common household hazardous items, such as paints, fluorescent light bulbs, pesticides, batteries and more
Residential-use only

## Slide 7
Notes: Sites are mixed size- limited space
Some owned
Some leased
One or two pre-crusher
Mixed entrance and exit

## Slide 8
Notes: 3 sites supersized size 2015

## Slide 9: Tour of South Wake Improvements

## Slide 10: Site 5 Improved Traffic
Congested two-way gate
Only two unloading spaces
Roll-off truck required to make
3-point turn at gate
Separate entrance and exit
Added unloading spaces
More space for backing residents and roll-off truck

## Slide 11: Site 3 Future Improvement
Small Convenience Center
Limited materials
Flood issue
No room to expand
Limited container space
Roll-off for Recycling & Metal require straight haul
Congested unloading
Pedestrians must cross over traffic to unload
Two-way gate

## Slide 12
Morrisville Public Works
Convenience Center
Multi-Material
HHW

## Slide 13: Durham County Solid Waste Division
Unincorporated Durham County
4 Solid Waste Convenience Sites
Curbside Recycling
Litter Control/Solid Waste Code Enforcement
Supported by Solid Waste Fee on unincorporated property tax bills ($164 in FY 22)

## Slide 14: Bahama & Rougemont Sites FY 21
132,000 Customers
1938 tons of MSW
536 tons of recycling
155 tons of yardwaste
Also collect: textiles, motor oil, cooking oil, scrap metal, white goods, & fluorescent bulbs

## Slide 15: Current Challenges
Approximately 5 minutes apart
Rougemont Site is very compact and leased from a private landowner
Bahama Site is larger, but poorly laid out and leased from the public school system.
Yard waste platform is one of top complaints.
Gravel driveways require frequent maintenance.

## Slide 16: Demand Study
1%, 1.5% and 2% growth
  Based of County population change
25-year projections
  200,000 visitors
  6,550 tons of material
  50 lbs waste per visitor
  10 lbs recyclables per visitor

## Slide 17: Program Optimization
Review existing data
  Traffic counts and peak hour
  Number of hauls
Community Input
  Customer Surveys at the two Sites
  Open House with Draft Plans and opportunity for comments

## Slide 18: New Northern Convenience Site
New site will be located in between existing locations
Access directly from 15/501 instead of secondary roads
Compaction of MSW, bulky and recyclables
Separate visitor traffic from hauling traffic
Back-in drop-off stalls
Utilize retaining wall as guardrail

## Slide 19: New Site Attendant Office
Restroom, Swap Shop, Computers, Observation Area/Meeting Room

## Slide 20: Design Details
2 lots to be combined for single 24 acre parcel
3.5 acres of disturbance
Environmental
  No impacts to floodplain or riparian buffer
  Proposed < 6% impervious area
  Stormwater Control Measures
    Maintain pre-development peak flows
    Reduce nutrient loading
On-site water supply and septic system

## Slide 21: Permitting
Special Use Permit was required for government facility in RR and RS-20 Zone
  Conformance with special requirements
    0.85 opacity buffer provided
    175’ between site and south property line
    150’ riparian buffer
  Harmony with surrounding properties
    Right-turn lane incorporated
    Existing median crossing utilized
    Coordinated with abutting property owner
    No adverse affect on public or property values

## Slide 22: Construction
Groundbreaking in April 2021
Completion anticipated January 2022
Current sites will operate until new site opens, then demolition will begin on the previous sites
Challenges include delayed delivery of equipment due to Covid, excess rock, and removal of tires

## Slide 23: Questions
Jeffrey S. Murray, PE, BCEE
Associate Vice President & Landfill Practice Lead
E: Jeffrey.Murray@hdrinc.com
P: 919.232.6682