## Slide 1: Management Challenges Associated w/ High Moisture Content in Landfills
VRA + SWANA Conference
VA Beach, Virginia
May 4, 2022

## Slide 2: Overview
Causes of High-Moisture “Wet” Landfills
Inventory of Primary Challenges
Circumstances Associated with Challenges
Potential Solutions & Protocols to Improve Circumstances

## Slide 3: Why are landfills retaining substantial quantities of free liquids elevated within waste matrix?
Reduced Porosity/Permeability Due to Waste Characteristics
Increased Waste Densities
Enhanced Biological Decomposition
Increased Quantities of Plastic Waste

## Slide 4: Why are landfills retaining substantial quantities of free liquids elevated within waste matrix?
Impermeable Zones Due to Design / Operations
“Protective Cover” - Placement of relatively low-permeable soil above the leachate drainage layer (typically a Geocomposite Drainage Net) and below the initial “fluff lift” of waste
Compacted Daily / Intermediate Cover Soil Layers

## Slide 6: Why are landfills retaining substantial quantities of free liquids elevated within waste matrix?
Precipitation Infiltration
Delayed Timing of Final Cap Installation
Reluctance to Utilize EGCs as Interim Cover

## Slide 8: Inventory of Primary Challenges
Extraction of Liquids From Waste Mass
Handling / Disposal of Extracted Liquids

## Slide 9: Circumstances Associated with Challenges – Secondary Problems
Insufficient LFG Collection System Effectiveness
- Odors
- Reduced LFGE Fuel
- Forcemain Clogging
- Non-Compliance
Slope Stability
Leachate Seeps

## Slide 10: Inventory of Primary Challenges
Is Landfill capable of handling/disposing of extracted liquids?
- Storage
- Transport
- Treatment
- Discharge/Disposal)
Limitation on Storage Tank Capacity
Limitation on Transport (Tanker Truck) Capabilities
Leachate Quantity Limitations
Leachate Quality Limitations

## Slide 11: Potential Solutions & Protocols to Improve Leachate Extraction
Mezzanine Leachate Collection Layers
  GDN, Aggregate, Sand, Perforated Piping
Infrastructure to Enhance Liquids Movement
Bottom Liner Augmentation Features
Deep Dewatering Wells
Multiple Sump Locations

## Slide 12: Dewatering Liquids Infrastructure
Dedicated Pneumatic Pump
Air Supply Line & Regulator
Liquids Discharge Forcemain
Isolation Valves
Air Release Valve
Air Compressor
Pump Stations

## Slide 13: Bottom Liner Augmentation Features
Objective: Enhanced LFG Extraction Combined with Passive Liquids Drainage
LFG Well Aggregate Target Pile
  “Rock Points” / “Gabion Cube”
Slope Collector Stub-Up Pipe
Bottom-Up Tiered Collectors
  Chimney Drains; Caisson Wells
Sustainable Imperatives & Initiatives Achieved:
  Reduced LFG & GHG fugitive emissions
  Reduced environmental risk (leachate seeps)
  Reduced energy consumption (fewer dewatering pumps)

## Slide 14: Leachate Collection & Liquid Management Systems
Increased Frequency of Cleaning:
  Jetting & Chemical Cleaning of Piping
  Cleaning & Servicing Wastewater Pumps
  Cleaning & Debris Removal within Sumps
More Cleanouts & Access Points
Anti-Foam Agent Injection from Totes
Electronic Descaling
Sustainable Imperatives & Initiatives Achieved:
  Reduced environmental risk of leachate release
  Reduced energy consumption
  Increased resiliency

## Slide 15: Potential Solutions & Protocols to Improve Handling/Treatment/Disposal
Solidify
Install Pre-Treatment Plant
  Nitrogen (NH3, TKN)
  BOD / COD
  TSS, TDS
  Other Constituents (PFAS, VOCs, etc.)
Leachate Evaporators
  VA - 6 Heartland Units
  SC – 2 Heartland Units & 4 Aptim Units
  NC – 1 Aptim Unit
Incur Additional Cost for T&D

## Slide 16: Conclusions
High-Moisture Conditions will continue to plague landfills
Some aspects are more within our control
Consider implementing BMPs both for liquids extraction as well as subsequent handling/disposal